Design of geometry of the staircase – example

Assignment (!!! This is just an example – use your values in the homework !!!)

- Height of the floor hk =3600 mm

- Depth of the main slab hs = 230 mm

- Depth of floor structure hf = 150 mm

- Thickness of cladding of the stairs hc = 30 mm

Dimensions of the staircase

- Ideal height of one step is 170 mm

- 3600 / 170 = 21,17 => 22 steps (2 flights with 11 steps)

- Height of one step h = 3600 / 22 = 164 mm

- Width of one step b = 630 – 2h = 302 mm

- DESIGN: Staircase with 164/300 mm steps, 2 flights, 11 steps in each flight

- Width of the flight – 1100 mm (in general, 1100 mm is the minimum width of the flight)

- Width of the gap between the flights – 200 mm (common value)

- Width of the landing – 1200 mm (should be at least “width of the flight + 100 mm)

- Width of the staircase is 1100*2+200 = 2400 mm

- Slope of the staircase is = arctan (164/300) = 28,66°

Scheme of the staircase

Preliminary check of the depth of the slab

- The staircase is considered as one-way slab with the span of 4500 mm. The slab will be simply supported => the depth should be at least 4500/25 = 180 mm.

- The depth of landings is the same as the depth of the main slab – 230 mm.

- The depth of flights can be obtained from the details of flight-landing connections (see the picture, see special file describing the construction of the detail). In our case, the depth is 220 mm.

- 230 mm > 180 mm and 220 mm > 180 mm => OK

Perpendicular and head clearance of the staircase

- Head clearance of the staircase should be more than 1500+750/cos = 1500+750/cos(28,66°) = 2355 mm and more than 2100 mm.

- Head clearance of our staircase is h1 = hk – hs – hf – h = 3600 – 230 – 150 – 164 = 3057 mm => OK.

- Perpendicular clearance of the staircase should be more than 750+1500*cos = 750+1500*cos(28,66°) = 2066 mm and more than 1900 mm.

- Perpendicular clearance of our staircase is h2 = h1cos = 3057cos(28,66°) = 2682 mm, => OK.